## Slide 1
16 May 2018
XXXXX
OrcaFlex Python Interface Development

## Slide 2
Introduction
I’m explaining code execution plan step by step in below slides.
Python code files location: Dropbox\0119 Programming\009 PythonOrcaFlex\0119-009-SPM\OrcaFlex

## Slide 3
Excel Spread sheet
Spread sheet location: Dropbox\0119 Programming\009 PythonOrcaFlex\0119-009-SPM\OrcaFlex\testData\SubmergedHoseData.xlsx
In this sheet we are gathered all necessary input design data
We are calculated all OrcaFlex properties in excel.
Hose connections and float locations.
Environmental loading conditions are also taken from these spreadsheet.
We are taken all necessary OrcaFlex input values from these spread sheet.

## Slide 4
Pre-processing
Define all input data in SubmergedHoseData.xlsx file. File location is 0119-009-SPM\OrcaFlex\testData
  1/ First we can run SampleOrcaFlexCode_18.py code, It builds' submerged hose 100year environmental condition base model. It contains 6 mooring lines(chains), CALM Buoy and 2 submerged hoses.
  2/ After completion of Step 1, Manually delete the chain 1 and chain 2 in base model, gives its names as SH_FM_100yr_R1.dat and SH_FM_100yr_R2.dat respectively. These files are the main files of failed mooring analysis process.
  3/ After that, we are going for 1year condition analysis. For these run SampleOrcaFlexCode_21_BAL.py code. This code open the OrcaFlex tanker model (TankerBaseModel_BAL.dat) file and adds all components(moorings and hoses)to this model. This is the SH 1yr ballast condition model file.
  4/ Run SampleOrcaFlexCode_21_BAL.py code. This code open the OrcaFlex tanker model (TankerBaseModel_FULL.dat) file and adds all components(moorings and hoses)to this model. This is the SH 1yr fully loaded condition model file

## Slide 5
Function files (Pre-processing)
Function files location: Dropbox\0119 Programming\009 PythonOrcaFlex\0119-009-SPM\OrcaFlex\lib\dataProvision
These function files extracts data from excel sheet and assigned these into OrcaFlex model.
When you are running above mentioned codes( previous slide), That code runs these function files and build the model.

## Slide 6
Post-processing
Post processing file location: Dropbox\0119 Programming\009 PythonOrcaFlex\0119-009-SPM\OrcaFlex\MainFunctionFile.py
Main function file contains below codes:
  1/ SamplePreProcessing.py
  2/ FileReadPostProcess.py
  3/ postprocessing.py
  1/ SamplePreProcessing.py code creates all its environmental loading condition models and runs the model analysis.
2/ FileReadPostProcess.py code, It reads all the sim files, extract required results and saves post processing code as postprocessing.py
3/ postprocessing.py these code extracts all the results in excel sheets and also produces required plots.

## Slide 7
Post Processing
In post processing process we are trying to write/edit code, at that time we can use FileReadPostProcess.py file only. It is the main post processing code file, it generates the repeated iteration/process and saves the code in these name postprocessing.py.

## Slide 8
Results & Plots
Results location: Dropbox\Programming\009 PythonOrcaFlex\0119-009-SPM\OrcaFlex\results \Results.xlsx
Plots location: Dropbox\Programming\009 PythonOrcaFlex\0119-009-SPM\OrcaFlex\results \Plots

## Slide 9
THANK YOU
For the opportunity to serve