## Slide 1
16 May 2018
XXXXX
OrcaFlex Python Interface Development

## Slide 2
Introduction
I’m explaining code execution plan step by step in below slides.
Now we are trying to convert results in jsonpickle format.
Python code files location: Dropbox\0119 Programming\009 PythonOrcaFlex\0119-009-SPM\OrcaFlex

## Slide 3
Pre-processing
Define all input data in SubmergedHoseData.xlsx file. File location is 0119-009-SPM\OrcaFlex\testData
  1/ First we can run SampleOrcaFlexCode_18.py code, It builds' submerged hose 100year environmental condition base model. It contains 6 mooring lines(chains), CALM Buoy and 2 submerged hoses.
  2/ After completion of Step 1, Manually delete the chain 1 and chain 2 in base model, gives its names as SH_FM_100yr_R1.dat and SH_FM_100yr_R2.dat respectively. These files are the main files of failed mooring analysis process.
  3/ After that, we are going for 1year condition analysis. For these run SampleOrcaFlexCode_21_BAL.py code. This code open the OrcaFlex tanker model (TankerBaseModel_BAL.dat) file and adds all components(moorings and hoses)to this model. This is the SH 1yr ballast condition model file.
  4/ Run SampleOrcaFlexCode_21_BAL.py code. This code open the OrcaFlex tanker model (TankerBaseModel_FULL.dat) file and adds all components(moorings and hoses)to this model. This is the SH 1yr fully loaded condition model file

## Slide 4
Post-processing
Now run the MainFunctionFile.py code. It saves all required results in excel (Results.xlsx) in results folder.
  Above code file contains SamplePreProcessing.py code, It creates all its environmental loading condition models and runs the analysis.
  And FileReadPostProcess.py code, It reads all the sim files, extract required results and saves post processing code as postprocessing.py.

## Slide 5
Post-processing (Improvements)
We are successfully get results in excel format. But now we are trying to convert these results into jsonpickle format.
I’m writing the code for jsonpickle formats. Its not converted the results. Can you please check the postprocessing.py code(line 736 to 748).
The code was running and not showing error messages.
We need to improve above code
I need your help on getting results in jsonpickle format.

## Slide 6
THANK YOU
For the opportunity to serve